Oregon Estuaries Survey Design

This document is presented as an example and recommended format for documenting a GRTS design.  It is recommended that this example be followed, prior to initiating efforts to produce a design to meet a particular objective.  Due to the randomization scheme within psurvey.design, each execution of the R code will produce a different set of sampling points and output files and will not exactly reproduce the example files.

Materials needed for this example:

R version 2.0 or later

psurvey.design package

R script or text file: OregonEstuary.R

Frame materials as ArcGis files:

Oregon2001Estuaries.dbf

Oregon2001Estuaries.prj

Oregon2001Estuaries.sbn

Oregon2001Estuaries.sbx

Oregon2001Estuaries.shp

Oregon2001Estuaries.shx

Example includes:

| Design |  | files produced |
| --- | --- | --- |
| 1 | Panel Over Time Sites – Two panels w/ 3 estuarine area size categories – equal number sites, 50 total, Over sample (50) | OREstuaryUnequalSites.dbf OREstuaryUnequalSites.prj OREstuaryUnequalSites.shp OREstuaryUnequalSites.shx |

An ArcGis map is included, Estuarine Design, as a visual aid for the resulting designs for this example.

Design File Documentation would routinely begin here:

### Contact:

Name

address of person requesting the design

Voice:

Fax:

email:

# Description of Sample Design for Panel Design

Target population:  All Oregon coastal estuaries of  less than 100 km2 in area.

Sample Frame: GIS Oregon coastal estuaries.

Survey Design: A Generalized Random Tessellation Stratified (GRTS) survey design for an area resource.  The GRTS design includes reverse hierarchical ordering of the selected sites.

Multi-density categories:  Small (<1 km2), medium (1-10 km2), large (10-100 km2)

Stratification:  None

Panels:  Two panels of equal size (25 each, total 50)

Expected sample size:  Approximately 17 sites in small estuaries, 17 sites medium estuaries, and 16 sites in large estuaries.

Oversample: 50 sites, approximately equal numbers for each category.

Site Use:  The base design has 50 sites in estuaries.  Sites are listed in SiteID order and must be used in that order.  All sites that occur prior to the last site used must have been evaluated for use and then either sampled or reason documented why that site was not used.  As an example, if 30 sites are to be sampled, then the first 30 sites in SiteID order would be used.

# Sample Frame Summary

The total estuarine area is km2

| Estuary Area | Number | Total Area (km2) |
| --- | --- | --- |
| Small | 34 | 2.056918 |
| Medium | 32 | 85.073934 |
| Large | 3 | 92.462461 |
| Total | 69 | 179.593314 |

# Site Selection Summary

| Unequal Sites | Small | Medium | Large | Sum |
| --- | --- | --- | --- | --- |
| Panel 1 | 9 | 11 | 5 | 25 |
| Panel 2 | 10 | 7 | 8 | 25 |
| Sum | 19 | 18 | 13 | 50 |
| Over sample | 15 | 16 | 19 | 50 |

Description of Sample Design Output:

The sites are provided as a shapefile that can be read directly by ArcMap.  The dbf file associated with the shapefile may be read by Excel.

The dbf file has the following variable definitions:

| Variable Name | Description |
| --- | --- |
| SiteID | Unique site identification (character) |
| arcid | Internal identification number |
| x | Albers x-coordinate |
| y | Albers y-coordinate |
| mdcaty | Multi-density categories used for unequal probability selection |
| weight | Weight (in meters), inverse of inclusion probability, to be used in statistical analyses |
| stratum | Strata used in the survey design |
| panel | Identifies base sample by panel name and Oversample by OverSamp |
| auxiliary variables | Remaining columns are from the sample frame provided |

### Projection Information –

PROJCS["NAD_1927_Albers",

GEOGCS["GCS_North_American_1927",

DATUM["D__North_American_1927",

SPHEROID["Clarke_1866",6378206.4,294.9786982]],

PRIMEM["Greenwich",0.0],

UNIT["Degree",0.0174532925199433]],

PROJECTION["Albers"],

PARAMETER["False_Easting",0.0],

PARAMETER["False_Northing",0.0],

PARAMETER["Central_Meridian",-96.0],

PARAMETER["Standard_Parallel_1",29.5],

PARAMETER["Standard_Parallel_2",45.5],

PARAMETER["Latitude_Of_Origin",23.0],

UNIT["Meter",1.0]]

### Evaluation Process

The survey design weights that are given in the design file assume that the survey design is implemented as designed.  That is, only the sites that are in the base sample (not in the over sample) are used, and all of the base sites are used.  This may not occur due to (1)  sites not being a member of the target population, (2) landowners deny access to a site, (3) a site is physically inaccessible (safety reasons), or (4) site not sampled for other reasons.  Typically, users prefer to replace sites that can not be sampled with other sites to achieve the sample size planned.  The site replacement process is described above.  When sites are replaced, the survey design weights are no longer correct and must be adjusted.  The weight adjustment requires knowing what happened to each site in the base design and the over sample sites.  EvalStatus is initially set to “NotEval” to indicate that the site has yet to be evaluated for sampling.  When a site is evaluated for sampling, then the EvalStatus for the site must be changed.  Recommended codes are:

| EvalStatus Code | Name | Meaning |
| --- | --- | --- |
| TS | Target Sampled | site is a member of the target population and was sampled |
| LD | Landowner Denial | landowner denied access to the site |
| PB | Physical Barrier | physical barrier prevented access to the site |
| NT | Non-Target | site is not a member of the target population |
| NN | Not Needed | site is a member of the over sample and was not evaluated for sampling |
| Other codes |  | Many times useful to have other codes. For example, rather than use NT, may use specific codes indicating why the site was non-target. |

### Statistical Analysis

Any statistical analysis of data must incorporate information about the monitoring survey design.  In particular, when estimates of characteristics for the entire target population are computed, the statistical analysis must account for any stratification or unequal probability selection in the design.  Procedures for doing this are available from the Aquatic Resource Monitoring web page given in the bibliography.  A statistical analysis library of functions is available from the web page to do common population estimates in the statistical software environment R.

### For further information, contact

Anthony (Tony) R. Olsen

USEPA NHEERL

Western Ecology Division

200 S.W. 35th Street

Corvallis, OR 97333

Voice: (541) 754-4790

Fax: (541) 754-4716

email: Olsen.Tony@epa.gov

Bibliography:

Diaz-Ramos, S., D. L. Stevens, Jr, and A. R. Olsen. 1996. EMAP Statistical Methods Manual. EPA/620/R-96/002, U.S. Environmental Protection Agency, Office of Research and Development, NHEERL-Western Ecology Division, Corvallis, Oregon.

Stevens, D.L., Jr. 1997. Variable density grid-based sampling designs for continuous spatial populations. Environmetrics, 8:167-95.

Stevens, D.L., Jr. and Olsen, A.R. 1999. Spatially restricted surveys over time for aquatic resources. Journal of Agricultural, Biological, and Environmental

Statistics, 4:415-428

Stevens, D. L., Jr., and A. R. Olsen. 2003. Variance estimation for spatially balanced samples of environmental resources. Environmetrics 14:593-610.

Stevens, D. L., Jr., and A. R. Olsen. 2004. Spatially-balanced sampling of natural resources in the presence of frame imperfections. Journal of American Statistical Association:99:262-278.

Web Page: http://www.epa.gov/nheerl/arm